## Slide 1
PROCESS REFERENCE MANUAL
The Physics Inside LandEvolve
Built mainly on the Landlab scientific library — with three custom components added where Landlab's ready-made pieces don't fit.
● 4 LANDLAB WRAPPERS
● 3 CUSTOM COMPONENTS

## Slide 2
THE FOUNDATION
Mostly Landlab, Lightly Customised
LandEvolve doesn't reinvent the science. The heavy geomorphology runs on Landlab — a peer-reviewed landscape-modelling library (Hobley et al. 2017; Barnhart et al. 2020). The app simply wraps each Landlab process in a thin, app-friendly component.
For three jobs Landlab does ship components — but they don't fit how LandEvolve works, so they were written as custom logic. Each slide names the Landlab component and the reason. (Full citations on the References slide.)
WRAPS A LANDLAB PROCESS
✓
Flow Accumulator
routes water, finds the rivers
✓
SPACE Eroder
Stream Power w/ Alluvium (rivers)
✓
Depth-Dependent Diffuser
hillslope soil creep
✓
Litho Layers
layered rock erodibility
CUSTOM LOGIC (LANDLAB'S PIECES DON'T FIT)
+
Precipitation
Landlab's rain is storm-scale, not long-term
+
Vegetation
Landlab's veg models biomass, not erosion
+
Tectonics (Uplift)
Landlab's tectonics model faults, not uplift rate

## Slide 3
READ THIS FIRST
The One Idea Behind It All
Almost all erosion comes from one simple idea: stream power.
A spot erodes faster when more water flows over it and when it is steeper. That's it.
“How much water” is the drainage area A — the size of the land draining into that spot. “How steep” is the slope S. K is how easily that ground wears down (soft mud vs hard granite).
Every component either feeds this idea, tunes its K, or pushes against it.
THE STREAM-POWER IDEA
erosion = softness × water × steepness
E = K · Aᵐ · Sⁿ
the same idea, written as maths
KEY: E erosion rate · K softness (erodibility) · A water (drainage area) · S slope · m, n how strongly water & slope count
RAIN + FLOW
decide the water
→
ROCK + PLANTS
decide the softness
→
SPACE
applies the idea
→
UPLIFT
pushes back up

## Slide 4
HOW THE DATA FLOWS
From GeoTIFF to a Living Grid
Your input is an elevation map — a GeoTIFF file, also called a DEM (Digital Elevation Model). Here's how it becomes a grid the components run on, and how it's saved back.
1
READ THE DEM
rasterio reads the elevation pixels. If the map is in degrees, it's auto-reprojected to metres (UTM) so slopes & areas are physical.
›
2
BUILD THE GRID
Every pixel becomes a node in a Landlab grid, its height stored in topographic__elevation. Edges are then set as boundaries (see below).
›
3
RUN THE LOOP
Each timestep the components read & write shared fields on the SAME grid — updating elevation, soil and drainage in place.
›
4
SAVE BACK
The final grid is written to a GeoTIFF using the saved real-world position, so results line up in QGIS / ArcGIS.
BOUNDARY CONDITIONS — WHERE WATER CAN LEAVE
The grid edges decide where water exits. LandEvolve closes every empty (NoData) cell and the whole perimeter, then opens just the single lowest edge cell as the outlet — the catchment's drain and base level. (If several edge cells tie for lowest, it auto-picks the pour point — the largest-drainage edge cell — instead of failing.)
Closed — NoData cells & perimeter: no flow across
Open outlet — the one lowest edge cell water drains to
THE SHARED GRID FIELDS
Components don't call each other — they read & write these named layers on the one grid:
topographic__elevation
soil__depth
bedrock__elevation
drainage_area
surface_water__discharge
water__unit_flux_in
K_sp

## Slide 5
COMPONENT · FLOW ACCUMULATOR
Flow Accumulator
● LANDLAB WRAPPER
WHAT IT DOES
Sends the rain downhill and works out, for every point, how much water flows through it (drainage area and discharge). This is the water SPACE then uses to erode — so nothing erodes without it.
WHAT YOU CAN DO WITH IT
▸ Routing: pick how water steps downhill — single steepest path, or D8 (any of 8 directions).
▸ Output: the river/stream network, plus drainage area & discharge on every cell.
▸ Lakes & pits: water trapped in hollows is automatically rerouted to the outlet.
HOW IT WORKS
Wraps Landlab's FlowAccumulator, then runs LakeMapperBarnes — a priority-flood pass (Barnes et al. 2014) — each step. It fills pits on a scratch surface and reroutes trapped water, so no fake sediment is added; without it flow dead-ends and SPACE dumps a runaway 'deposition' spike.
WHAT IT WORKS OUT
water gathered = all the rain flowing in from uphill
A = Σ (upstream cell areas)
the drainage area feeding each point
Q = Σ (R × cell area)
the water discharge passing through
KEY: A drainage area · Q discharge · R rain/runoff · Σ means “add up”
⚙ YOU SET FOR YOUR SITE
flow_director choose routing — Steepest or D8
✓ USUALLY LEFT AT DEFAULT
runoff_rate default 1.0; dropped when Precipitation or Vegetation is on
LakeMapperBarnes pit-fill, auto-configured
depression handling automatic

## Slide 6
COMPONENT · SPACE ERODER
SPACE Eroder
● LANDLAB WRAPPER
WHAT IT DOES
The river engine. SPACE stands for Stream Power with Alluvium Conservation and Entrainment. Using the water (from Flow Accumulator) and the slope, it carves bedrock, picks up loose sediment where flow is strong, and drops it where flow slows — while keeping track of the soil layer sitting on the bedrock.
WHAT YOU CAN DO WITH IT
▸ Two eroders: standard Space, or SpaceLargeScaleEroder (tougher for big grids).
▸ Bare-rock rivers: thin soil → water cuts into bedrock.
▸ Sediment-bed rivers: thick soil → channels build up & rework alluvium.
HOW IT WORKS
Wraps Landlab's SPACE eroder (Shobe et al. 2017). Each step the app feeds in the right softness K (from rock type + plants); thick soil shields the bedrock, so bare ground wears its rock but covered ground doesn't.
SPACE IN PLAIN WORDS + MATHS
scoop up soil = strong flow (less if soil is deep)
Eₛ = K_sed · Qᵐ · Sⁿ · (1 − e^(−H/H*))
carve rock = strong flow (only where soil is thin)
E_r = K_br · Qᵐ · Sⁿ · e^(−H/H*)
soil change = what's dropped − what's scooped
∂H/∂t = D/(1−φ) − Eₛ
KEY: Eₛ soil scooped · E_r rock carved · K softness · Q water · S slope · m,n strength of water & slope · H soil depth · H* shield scale · D deposited · φ pore space
⚙ YOU SET FOR YOUR SITE
K_br, K_sed bedrock & sediment softness (your rock)
v_s settling velocity — controls deposition
soil_depth starting soil thickness over bedrock
✓ STANDARD VALUES — used across studies
m_sp, n_sp = 0.5, 1.0 (Whipple & Tucker 1999)
H_star shield depth ~0.1–0.5 m (Shobe+ 2017)
phi porosity ≈ 0.3 (Shobe+ 2017)

## Slide 7
COMPONENT · HILLSLOPE DIFFUSER
Depth-Dependent Diffuser
● LANDLAB WRAPPER
WHAT IT DOES
Moves soil slowly downhill on slopes — the gentle creep that rounds off sharp ridges and fills in hollows, even where there are no rivers. It changes the land surface on hillslopes; SPACE handles the channels.
WHAT YOU CAN DO WITH IT
▸ Rounds off sharp ridges into smooth, soil-mantled hillslopes.
▸ Fills in hollows as soil creeps down and collects.
▸ Softens steep scarps & terraces over time.
HOW IT WORKS
Wraps Landlab's DepthDependentDiffuser (Johnstone & Hilley 2015). Soil drifts faster on steeper slopes, but only where there's soil to move — bare bedrock doesn't 'flow'. Landlab's diffuser has no stability check of its own (explicit diffusion needs dt ≤ cell²/(4·K)); this wrapper auto-substeps internally so results stay correct at any dt or grid resolution you pick.
SOIL CREEP, IN PLAIN WORDS + MATHS
soil creep = steepness × (more where soil is deep)
q_s = −K · ∇z · (1 − e^(−H/H*))
how much soil drifts downhill
∂z/∂t = −∇·q_s
ground rises/falls as soil arrives or leaves
KEY: q_s soil moved · K creep rate · ∇z slope (∇ = change over distance) · H soil depth · H* decay depth
⚙ YOU SET FOR YOUR SITE
linear_diffusivity hillslope creep rate — your soil & climate
✓ USUALLY LEFT AT DEFAULT
decay depth ≈ 0.5 m (typical default)

## Slide 8
COMPONENT · LITHOLOGY
Litho Layers
● LANDLAB WRAPPER
WHAT IT DOES
Sets how hard the rock is at the surface — the softness K that SPACE erodes with — and updates it as erosion digs down and exposes deeper layers. This is how different rock types erode at different rates.
WHAT YOU CAN DO WITH IT
▸ You build the rock stack: each layer's depth, type, and softness.
▸ Hard over soft: a tough cap-rock makes cliffs & plateaus.
▸ Layered: alternating hard/soft beds erode unevenly as they're bared.
HOW IT WORKS
Wraps Landlab's Lithology submodule (Barnhart et al. 2018). Every step it refreshes the surface softness K to whatever rock is currently exposed, so SPACE always erodes the correct material.
WHAT IT TRACKS
surface softness = softness of the rock now exposed
layers: z0s = [10, 30, …] m
ids = [rock₁, rock₂, …]
K(node) = softness[ exposed rock ]
refreshed every step → feeds SPACE
KEY: z0s layer base depths (m) · ids rock-type IDs · K surface softness (erodibility)
⚙ YOU SET FOR YOUR SITE
z0s, ids layer depths & rock types — from geology
attrs {K_sp} softness per rock — from lithology data
✓ USUALLY LEFT AT DEFAULT
layer_type = MaterialLayers (fixed)
rock_id base type for new sediment

## Slide 9
COMPONENT · PRECIPITATION
Precipitation
● CUSTOM LOGIC
WHAT IT DOES
Sets how much rain (runoff) lands on each cell — the water that Flow Accumulator turns into discharge, which drives SPACE's erosion. So this is the climate dial behind everything.
WHAT YOU CAN DO WITH IT
▸ Uniform: the same steady rainfall everywhere.
▸ Spatial: rainfall varies by place, from a map (e.g. wetter mountains).
▸ Trend: rainfall rises or falls over time (climate change).
▸ Stochastic: random wet & dry periods.
⚠ LANDLAB HAS COMPONENTS — WHY NOT USE THEM?
Landlab's PrecipitationDistribution & SpatialPrecipitationDistribution generate individual-storm sequences. Our timesteps are long-term (≫ one storm), so we model effective climate, not storms — hence custom.
RUNOFF & ITS FOUR MODES
runoff = rainfall × fraction that runs off
Uniform: r = P · C
Spatial: r from a rainfall map
Trend: P grows/shrinks over time
Stochastic: random wet & dry periods
Why default runoff = 1?
It's the classic convention: runoff = 1 makes
discharge = drainage area. Keep it if your K assumes
it; use realistic runoff if you set K independently
(e.g. from rock hardness). The app supports either way.
⚙ YOU SET FOR YOUR SITE
mode Uniform / Spatial / Trend / Stochastic
precipitation mean rainfall rate for your climate
✓ USUALLY LEFT AT DEFAULT
runoff_coefficient fraction that runs off; 1.0 = all of it (see note)
variability, final_ only for Stochastic / Trend modes

## Slide 10
CLEARING UP THE RUNOFF NUMBERS
Runoff & Discharge, Explained
THE WHOLE IDEA IN ONE LINE
Q = R × A
discharge = runoff (water per cell) × drainage area (cells draining in)
1
Flow Accumulator — runoff_rate
One flat runoff number for the whole grid (default 1.0). The simple baseline used when you're not modelling climate.
2
Precipitation — the climate way
Sets runoff per cell from climate: R = P × C (rainfall × fraction that runs off). It overrides the flat number.
Both write the SAME field — water__unit_flux_in. Precipitation just replaces Flow Accumulator's flat 1.0 with a climate pattern.
SO WHY IS THE DEFAULT R = 1.0?
With R = 1, discharge equals drainage area (Q = A) — the classic stream-power convention where area stands in for water (K is the ground's softness / erodibility). It's the default simply because it's convenient.
Keep R = 1 only if your K was calibrated for it (most literature values were). If you set K your own way — e.g. from rock hardness — you're free to use realistic runoff instead. The app doesn't tie you to one erodibility method; runoff still affects how much erosion you get either way.
Using area as a proxy for discharge (uniform-runoff assumption): Howard (1994) · Whipple & Tucker (1999) · Wobus et al. (2006).

## Slide 11
THE SAME IDEA, NO JARGON
Runoff, in Plain Words
1
Discharge = runoff × area
The water rushing through a spot is just all the uphill water added together.
2
Area stands in for water
The erosion formula uses area, not water. That only works if every cell gets the same rain — so runoff is set to 1, making water = area.
3
Runoff = 1 is just a baseline
Setting runoff to 1 makes water = area — a normalisation for the maths, not a real rainfall amount. (The runoff_coefficient is separate: 1.0 there does mean 100% runs off.)
4
Keep it, or change it? Your call
If your K (erodibility) came from a study that assumed runoff = 1, keep runoff = 1 so they match. If you set K your own way — e.g. from rock hardness — you can use realistic runoff instead. The app supports either.
5
Two names, one knob
Flow Accumulator's runoff_rate and Precipitation's runoff_coefficient write the SAME water layer — Precipitation just swaps the flat 1.0 for a real climate pattern.

## Slide 12
COMPONENT · VEGETATION
Vegetation
● CUSTOM LOGIC
WHAT IT DOES
Plants armour the ground. Each cover type re-tunes three things the eroders use, per cell: the erodibility K in SPACE (how easily it erodes), the hillslope creep rate, and how much rain runs off. Bare ground erodes fast; forest barely erodes.
WHAT YOU CAN DO WITH IT
▸ Static: pick one ground cover for the whole run — bare, grass, shrub or forest.
▸ Dynamic (Transition): switch cover at a chosen year — e.g. grass → trees (regrowth), or forest → cleared (deforestation, wildfire).
⚠ LANDLAB HAS COMPONENTS — WHY NOT USE THEM?
Landlab's Vegetation component simulates plant biomass growth via soil-moisture ecohydrology — far more than we need. We only need per-cell erosion / creep / runoff multipliers, so this is custom.
HOW PLANTS CHANGE THE NUMBERS
new value = base value × a plant factor
softness: K → K × m_K
creep: D → D × m_D
runoff: r → r × m_runoff
each factor depends on the plant type
KEY: m_K softness factor · m_D creep factor · m_runoff runoff factor (one set per plant class)
⚙ YOU SET FOR YOUR SITE
vegetation_mode Static or Transition
class factors the m_K, m_D, m_runoff per cover type
✓ USUALLY LEFT AT DEFAULT
multipliers = 1.0 means 'no effect' (bare baseline)
transitions only if cover changes over time

## Slide 13
COMPONENT · TECTONICS
Tectonics (Uplift)
● CUSTOM LOGIC
WHAT IT DOES
Raises the inner land a little each step (it adds height to the elevation field). This is the force that builds relief by competing with erosion — without it, erosion alone would wear the whole landscape flat.
WHAT YOU CAN DO WITH IT
▸ Uniform: the whole region rises at one steady rate (block uplift).
▸ Spatial: different parts rise at different rates, from a map — tilting, or faster-rising blocks.
⚠ LANDLAB HAS COMPONENTS — WHY NOT USE THEM?
Landlab's tectonic components (NormalFault, ListricKinematicExtender, Flexure, gFlex) model specific fault or flexure mechanisms, not a general uplift rate. Most landscape-evolution studies just apply an uplift rate — exactly what this does.
RAISING THE LAND, IN PLAIN WORDS + MATHS
new height = old height + uplift speed × time
z(inner) += U · dt
the land surface rises
edges stay fixed → relief grows
uplift recorded → removed from result map
KEY: z land height · U uplift rate (height per unit time) · dt time step length
⚙ YOU SET FOR YOUR SITE
uplift_rate tectonic rate — estimate for your region
mode Uniform or Spatial
✓ USUALLY LEFT AT DEFAULT
uplift_raster only for Spatial (per-cell) uplift

## Slide 14
PUTTING IT TOGETHER
One Timestep, Step by Step
Components never call each other — they read and write one shared landscape, in a fixed order. Each step:
1
Precipitation
sets the rain (runoff)
2
Vegetation
adjusts runoff & softness
3
Flow Accumulator
routes water, finds rivers
4
Diffuser
soil creeps down slopes
5
SPACE
rivers erode & deposit
6
LithoLayers
exposes the next rock layer
7
Tectonics
raises the land
WHY THIS ORDER?
Rain is set before the water is routed.
Plants adjust the softness K before SPACE erodes.
Rock layers refresh after erosion, so the next step sees newly bared rock.
Uplift comes last: erode first, then raise.

## Slide 15
REFERENCE
Standard Values from the Literature
These parameters are usually left at conventional default values rather than estimated per site. (The site-specific ones — K, v_s, diffusivity, uplift, soil depth — depend on your rock & climate and aren't tabulated here.)
Parameter
Symbol
Standard value
Source
Discharge (area) exponent
m_sp
0.5
Whipple & Tucker (1999)
Slope exponent
n_sp
1.0
Whipple & Tucker (1999)
Sediment cover / shield depth
H*
~0.1–0.5 m
Shobe et al. (2017)
Sediment porosity
φ
≈ 0.3
Shobe et al. (2017)
Soil-transport decay depth
dₛ
~0.5 m
model default (Johnstone & Hilley 2015)
Runoff coefficient (baseline)
C
1.0
model normalisation
Author–year sources above are listed in full on the References slide at the end.

## Slide 16
CHEAT SHEET
Quick Reference
Process
Type
In plain words
Key knob
Precipitation
Custom
Sets the rain — Landlab's rain is storm-scale, not long-term
precipitation
Vegetation
Custom
Plants tune erosion — Landlab's veg models biomass instead
veg class
Flow Accumulator
Landlab
Routes water downhill, finds the rivers
flow_director
Diffuser
Landlab
Soil slowly creeps down slopes
linear_diffusivity
SPACE Eroder
Landlab
Rivers carve rock & move sediment
K_br, K_sed
LithoLayers
Landlab
Exposes layered rock of different hardness
z0s, ids
Tectonics
Custom
Raises the land — Landlab's tectonics model faults, not uplift rate
uplift_rate
Built mostly on Landlab; custom pieces cover the three jobs Landlab's own components don't fit — climate, vegetation, and uplift.

## Slide 17
THE WHOLE PICTURE
Seven processes, one shared landscape, stepped forward through time.
One simple idea: erosion = softness × water × steepness
Mostly Landlab: Flow, SPACE, Diffuser, Lithology
Custom where Landlab's own pieces don't fit: rain, plants, uplift
They never call each other — they share one landscape, in order

## Slide 18
SOURCES
References
LANDLAB FRAMEWORK
Hobley, D.E.J. et al. (2017). Creative computing with Landlab. Earth Surf. Dynam. 5, 21–46.
Barnhart, K.R. et al. (2020). Landlab v2.0. Earth Surf. Dynam. 8, 379–397.
COMPONENTS USED
Shobe, C.M., Tucker, G.E. & Barnhart, K.R. (2017). The SPACE 1.0 model. Geosci. Model Dev. 10, 4577–4604. [SPACE eroder]
Barnes, R., Lehman, C. & Mulla, D. (2014). Priority-flood depression filling. Computers & Geosciences 62, 117–127. [LakeMapperBarnes]
Barnhart, K.R., Glade, R.C., Shobe, C.M. & Tucker, G.E. (2018). Lithology Landlab submodule. J. Open Source Softw. 3(30), 979. [LithoLayers]
Johnstone, S.A. & Hilley, G.E. (2015). Lithologic control on hillslope form. Geology 43(1), 83–86. [DepthDependentDiffuser]
Barnhart, K.R., Glade, R.C., Shobe, C.M. & Tucker, G.E. (2019). terrainbento 1.0. Geosci. Model Dev. 12, 1267–1297. [parameter defaults]
THEORY & STANDARD PARAMETER VALUES
Howard, A.D. (1994). A detachment-limited model of drainage-basin evolution. Water Resour. Res. 30(7), 2261–2285.
Whipple, K.X. & Tucker, G.E. (1999). Dynamics of the stream-power incision model. J. Geophys. Res. 104(B8), 17661–17674.
Wobus, C. et al. (2006). Tectonics from topography. GSA Special Paper 398, 55–74.